## Slide 1
BD9E151NUX-E2EVK-101 Measurement Report
September 22, 2014
Hosted by: Xuan Dang

## Slide 2
Equipment list
Regulated DC Power Supply
  QJE QJ3005XE (0-30V/5A).
Multimeter:
  Fluke 87V True RMS.
  Fluke 106.
Oscilloscope
  Rigol DS1102E.
Electronic Load
  B&K BK8500.
Current probe
  RP1001C.

## Slide 3
Functional Test
Test case 1 procedure with electronic load BK8500
  Turn on the DC Supply. Set output of the DC Supply in range from 6V to 28V and turn it off. Connect DC the Supply to: [+]VIN(TP1) and [-]GND(TP2) of evaluation board.
  Connect Electronic Load to: [+]VOUT(TP3) and [-]GND(TP4). Power on Electronic Load, set input of Electronic Load to 1.2A.
  Turn on the DC Supply.
  Turn on load.
  Move header J1 to turn EN on.
Result:
  VIN = 6V to 28V.
  Vout = 0V/ 0.02A. Test fail.
  The output current with electronic load BK8500 exceed ~1.75A that cause OCP (over current protection) active and shut down IC. See next slide for output current measurement.

## Slide 4
Functional Test (cont.)
IOUT 1A/Div. (DC)
VEN 5V/Div. (DC)
Time 2ms/Div.
Output current ~1.75A which cause OCP active and shut down IC

## Slide 5
9/22/2014
PTH Solutions Confidential
5
Functional Test (cont.)
Test case 2 procedure with power resistor load 4.6 Ohms:
  Turn on the DC Supply. Set output of the DC Supply in range from 6V to 28V and turn it off. Connect DC the Supply to: [+]VIN(TP1) and [-]GND(TP2) of evaluation board.
  Connect 4.6 Ohm Resistor to: [+]VOUT(TP3) and [-]GND(TP4).
  Turn on the DC Supply.
  Move header J1 to turn EN on.
Result:
  VIN = 6V to 28V.
  Vout = 4.95V/ 1.1A. Test pass.
  No output current glitch with power resistor load 4.6 Ohms. So the OCP is not active like test case 1. See next slide for measurement result

## Slide 6
Functional Test (cont.)
IOUT 1A/Div. (DC)
VEN 5V/Div. (DC)
Time 20ms/Div.

## Slide 7
Hot Plugging Test
Test case 1
  VIN = 22V.
  IOUT = 1.2A.
  With diode D2: SMAJ20A.
Result:
IIN_MAX= 99.2A.
VIN peak transient voltage is 31V > VIN Maximum Rating (30V). Test fail
VIN 10V/Div. (DC)
IIN 20A/Div. (AC)
Time 5us/Div.

## Slide 8
9/22/2014
PTH Solutions Confidential
8
Hot Plugging Test( Cont.)
Test case 2
  VIN = 22V.
  IOUT = 0A.
  With diode D2: SMAJ20A.
Result:
IIN_MAX= 102A.
VIN peak transient voltage is 31V > VIN Maximum Rating (30V). Test fail
VIN 10V/Div. (DC)
IIN 20A/Div. (AC)
Time 5us/Div.

## Slide 9
9/22/2014
PTH Solutions Confidential
9
9/22/2014
PTH Solutions Confidential
9
Hot Plugging Test( Cont.)
Test case 3
  VIN = 21V.
  IOUT =1.2A.
  With diode D2: SMAJ22A.
Result:
IIN_MAX= 94.4A.
VIN peak transient voltage is 32V > VIN Maximum Rating (30V). Test fail
VIN 10V/Div. (DC)
IIN 20A/Div. (AC)
Time 5us/Div.

## Slide 10
Chart: Quiescent Current
| 0 | 0.5 | 1 | 1.5 | 2 | 2.5 | 3 | 3.5 | 4 | 4.5 | 5 | 5.5 | 6 | 6.5 | 7 | 7.5 | 8 | 8.5 | 9 | 9.5 | 10 | 10.5 | 11 | 11.5 | 12 | 12.5 | 13 | 13.5 | 14 | 14.5 | 15 | 15.5 | 16 | 16.5 | 17 | 17.5 | 18 | 18.5 | 19 | 19.5 | 20 | 20.5 | 21 | 21.5 | 22 | 22.5 | 23 | 23.5 | 24 | 24.5 | 25 | 25.5 | 26 | 26.5 | 27 | 27.5 | 28
 | 0 | 0.5 | 1.1 | 8.2 | 31.6 | 99.4 | 130.1 | 196.2 | 266.8 | 390.5 | 472.6 | 950 | 1006 | 1084 | 1254 | 1331 | 1348 | 1248 | 1102 | 1105 | 1107 | 1102 | 1092 | 1083 | 1073 | 1062 | 1053 | 1044 | 1037 | 1030 | 1024 | 1021 | 1018 | 1015 | 1013 | 1014 | 1012 | 1010 | 1008 | 1004 | 1001 | 999 | 994 | 990 | 987 | 983 | 980 | 978 | 977 | 976 | 976 | 975 | 976 | 976 | 976 | 976
Circuit Quiescent Current Measurement
Test condition
  VIN = 0-28V.
  Room temperature 25oC.

## Slide 11
Efficiency Measurements
Test condition
  VIN = 12V.
  VOUT = 5V.
  With SMAJ26A.
  Room temperature 25oC.
Chart: IOUT (mA)
| 0 | 25 | 50 | 100 | 150 | 200 | 250 | 300 | 350 | 400 | 450 | 500 | 550 | 600 | 650 | 700 | 750 | 800 | 850 | 900 | 950 | 1000 | 1050 | 1100 | 1150 | 1200
 | 0 | 76.2 | 84.7 | 89.7 | 91 | 92 | 92.3 | 93.1 | 93.2 | 93 | 93.3 | 93 | 93.4 | 93.2 | 93.4 | 92.9 | 93.1 | 93 | 92.6 | 92.6 | 92.5 | 92.4 | 92.3 | 91.8 | 91.8 | 91.8
 | 1
 | 1
 | 1

## Slide 12
Load Response Measurements
Load response characteristic
(VIN=12V, VOUT=5V, IOUT=0A  1.2A)
VOUT 100mV/Div. (AC)
IOUT 0.5A/Div. (DC)
Time 10ms/Div.

## Slide 13
Load Response Measurements (cont.)
Load response characteristic
(VIN=12V, VOUT=5V, IOUT=1.2A  0A
VOUT 100mV/Div. (AC)
IOUT 0.5A/Div. (DC)
Time 10ms/Div.

## Slide 14
Ripple Response Measurements
VOUT Ripple voltage
(VIN=12V, VOUT=5V, IOUT=0A)
VSW 5V/Div. (DC)
VOUT 10mV/Div. (AC)
Time 2ms/Div.

## Slide 15
Ripple Response Measurements (cont.)
VOUT Ripple voltage
(VIN=12V, VOUT=5V, IOUT=1.2A
VSW 5V/Div. (DC)
VOUT 10mV/Div. (AC)
Time 2ms/Div.